# OS LED strips Manual
LED strips for coaches and universal 12V LED strips

## 🛠️ Overview
LED-based lighting strips tailored for model railway passenger coaches. These strips are optimized for DCC layouts and offer both flexibility and simplicity in installation.

## 🧩 Variants
### 🔸 LED Strip Modules (19cm, 22cm, 25cm, 28cm)
- Designed for internal mounting inside rolling stock
- Integrated constant current source to maintain brightness during voltage dips
- Potentiometer allows manual brightness adjustment
- Two solder pads for attaching an external 220uF 25V capacitor
- Power pass-through solder pads at the ends allow daisy-chaining
- For use with digital/DCC-powered trains only
### 🔹 Universal Power Pack Module
- Meant for driving standard 12V LED strip rolls
- Accepts DCC signal on input pads
- Outputs stable +12V and GND for external strip lighting
- Also contains constant current circuitry for consistent lighting